## Slide 1: VSkin: Sensing Touch Gestures on Surfaces of Mobile Devices Using Acoustic Signals
Ke Sun, Ting Zhao, Wei Wang, and Lei Xie
MobiCom'18 Nov 1st, 2018
State Key Laboratory for Novel Software Technology
Nanjing University

## Slide 2: Motivation
Touchscreen gestures: de facto standard user interface
Only on the touchscreen!

## Slide 3: Motivation
Occlusion problems !

## Slide 4: Motivation
User intentions confusion!
Click or Scroll?

## Slide 5: Motivation
Bad experience!
Too many buttons
on the screen

## Slide 6: If we can enable the touch gestures on all surfaces of the mobile devices?

## Slide 8: Basic idea
VSkin utilizes the built-in speakers
and microphones to send and receive ultrasound signals for touch-sensing.
Speaker
Mic
Mic
Speaker
Mic
Mic

## Slide 9: Basic idea
Structure-borne sound
LOS air sound
Reflection air sound

## Slide 10: Basic idea
When performing touch gestures:
Structure sound pattern changes:
Touch detection
Reflection air path distance changes:
Movement measurement

## Slide 11: Challenge 1
How to separate the structure-borne and the air-borne sound signals?

## Slide 12: Basic idea: Delay difference
Structure-borne sound
High speed
Low delay
LOS air sound
Low speed
Medium delay
Reflection air sound
Long distance
Large delay

## Slide 13: Basic idea: Delay difference
Challenge: Delay difference is too small (<0.34 ms) !
Too small interval
to hear the echo
Solution: Transmission signal design
Structure sound
LOS sound
Reflect sound
Notes: 5A

## Slide 14: Transmission signal design
Choose ‘explicit’ signal
High resolution
High SNR
Narrow inaudible range
Phase information
ZC sequence

## Slide 15: Transmission signal design
Autocorrelation of baseband ZC sequence
ZC sequence: near-optimal auto-correlation function
Narrow main lobe width
High gain
Low side lobe

## Slide 16: Sound Propagation Separation
Structure sound
LOS sound
Reflect sound
Mixed !
Use cross-correlation to estimate impulse response
Peaks indicate propagation paths

## Slide 17: Sound Propagation Separation
Bottom Mic
Top Mic
Structure-borne sound
LOS air sound
Reflection air sound

## Slide 18: Sound Propagation Separation
Bottom Mic
Top Mic
Static delay:
Structure-borne path
LOS air path
Calibration
Dynamic delay:
Reflection air path
Dynamic change

## Slide 19: Challenge 2
How to measure the path coefficient (phase & amplitude) of single path?
Notes: 科普

## Slide 20: Path coefficient
I/Q trace  Phase & amplitude
Phase change: path distance
Amplitude: path strength
Path coefficient: I/Q trace for certain delay

## Slide 21: Challenge 2
Tradition: One frame obtains one result for signal path.
I/Q trace when moving the hand
Path coefficient sampling rate is not enough when moving fast!

## Slide 22: Basic idea: Moving window
ZC sequence
Receive sequence
Receive sequence
Receive sequence
Receive sequence
ZC sequence
ZC sequence
ZC sequence
3
4
1
2
Only 1 result for 1 frame！

## Slide 23: Basic idea: Moving window
ZC sequence
Receive sequence
Receive sequence
Receive sequence
Receive sequence
ZC sequence
ZC sequence
ZC sequence
High sampling rate！
...
1
2
3

## Slide 24: Challenge 3
How to measure the movement and detect the touch?

## Slide 25: Movement measurement
Reflect path delay changes when moving
Notes: 原因

## Slide 26: Movement measurement
Select the delay of reflection path based on differential IR
Move away
Move towards
Magnitude of differential IR estimations
Notes: 原因

## Slide 27: Movement measurement
Additive Noise Mitigation:
Extended Kalman Filter
Phase Based Measurement:
Curvature-based estimation

## Slide 28: Touch detection
Magnitude of differential IR estimations
at 1 cm away from speaker
Magnitude of differential IR estimations at 7 cm away from speaker
Touch
Release
Touch
Release
Unique patterns for different positions
Delay of the peak in differential IR estimation to determine the touch position
Notes: 加图

## Slide 29
Real-time APP works on COTS mobile phone:
Use rear speaker, top microphone, and bottom microphone
Enable touch gestures, e.g., scrolling, swiping, and tapping
Conduct on four different kinds of smartphones
Implementation
Speaker
Mic
Mic

## Slide 30
Average movement distance error of 3.59 mm
Movement distance with speeds from 2 cm/s to 12 cm/s
Finger movement accuracy

## Slide 31
Robust for different diameters and holding styles
Robust to other interfering movements
Robust to background audible acoustic noises
Finger movement robustness
Jamming distance

## Slide 32
Touch detection rate of 98% at the back of the phone
Average accuracy of 87.82% for classifying touches to three different regions of the phone.
Touch measurement accuracy

## Slide 33
Only 193.1ms slower than the touchscreen.
Case study: VSkinScrolling

## Slide 34
Only 112.7ms slower than the screen
Direction recognition accuracy of 94.5%
Case study: VSkinSwiping

## Slide 35
Sensing touch gestures on all surfaces of mobile devices by separating the structure-borne and the air-borne sound signals.
Different kinds of touch gestures
swiping, tapping, scrolling
Fine-grained gesture measurement
  mm-level distance accuracy, speed robustness
Low computational cost
real time APP works on mobile devices
Conclusion

## Slide 36
Thank you
Q&A