## Slide 1: StealthyIMU: Extracting Permission-protected Private Information from Smartphone Voice Assistant using Zero-Permission Sensors
Ke Sun, Chunyu Xia, Songlin Xu, Xinyu Zhang
NDSS’23, Mar 1st, 2023
University of California, San Diego

## Slide 2: Speech Eavesdropping on Smartphone
Microphone
Motion Sensor
No permission required
Permission required
Attacker
Only loudspeaker-rendered speech signals traveling through a solid surface can create noticeable impacts on motion sensors [1].
[1] Speechless: Analyzing the threat to speech privacy from smartphone motion sensors, S&P’18
Victim
Motion Sensor Signals
(MSS)
Notes: Traditionally, adversaries can use the microphone on the smartphone to eavesdrop on the victim.
However, the microphone permission has been protected by the smartphone OS permission.
In comparison, the motion sensors are zero-permission sensors, which are accessible by any app on the mainstream mobile OS to facilitate applications like Auto-rotate screen. Recently some papers show that they can potentially create a side channel to eavesdrop on the speech of the victim by capturing the vibration induced by speech signals. However, recent research found that only loudspeaker-rendered speech signals traveling through a solid surface can create noticeable impacts on motion sensors. Therefore, the threat of such a side-channel eavesdropping attack is not that significant since it can only capture the speech from the loudspeaker.

## Slide 3: Limitations of Prior works
Motion Sensor:
Low sampling rate (<= 500 Hz)
Low Signal-to-Noise Ratio (SNR)
Additional interference
Achieve low-risk task
Classifying a small set of digits and hot words [2,3]
Partially recover the speech signals [4]
In ideal scenario
Small number of users in the dataset (<20 users) [2][3][4]
Training and testing with the same group of users [2][3][4]
[2] Learning-based practical smartphone eavesdropping with built-in accelerometer, NDSS’20
[3] Spearphone: a lightweight speech privacy exploit via accelerometer-sensed reverberations from Smartphone loudspeakers, WiSec’21
[4] AccEar: Accelerometer Acoustic Eavesdropping with Unconstrained Vocabulary, S&P’22
Notes: Besides, since the motion sensors are not designed for speech eavesdropping. They also have a limited low sampling rate, low SNR, and additional interference compared to the microphone. This results in that they can only capture the fundamental frequency of human speech less than 250 Hz and has low SNR and large interference.

## Slide 4: Will this threat model pose a real privacy threat to victims?
Loudspeaker
Motion Sensor
No permission required
Attacker
Victim
Extracting Permission-protected Private Information from Smartphone Voice-User Interface (VUI) responses.

## Slide 5: StealthyIMU Threat Analysis
Reading permissions granted by VUI app
Alarm
Reminder
Phone
SMS
Calendar
Contacts
Locations
Search history
Voicemail
Billing
etc
Voice Assistant responses
contain the permission-protected
private information.
Motion Sensor
No permission required
Attacker

## Slide 6: StealthyIMU Threat Model
Victim
Set a reminder to check my bank account XXXX.
Got it, check
bank account XXXX.
Motion Sensor
No permission required
Attacker
Apple Siri,
Google Assistant
Type: Reminder
Intents:
Check bank account
XXXX

## Slide 7: StealthyIMU Threat Model
In 600 feet use the right
lane to turn right onto
Hollywood Boulevard.
Motion Sensor
No permission required
Attacker
GPS Trace
Type: Navigation
Intents:
Turn right
Names:
Hollywood Boulevard

## Slide 8: Inferring privacy from a single VUI response: problem statement
Traditional Spoken Language Understanding (SLU) system for VUI
[5] Snips Voice Platform: an embedded Spoken Language Understanding system for private-by-design voice interfaces

## Slide 9: Comparison between SLU for VUI and StealthyIMU
 | SLU for VUI | SLU for StealthyIMU
Goal | Extract the request from speech | Extract the privacy from VUI response induced MSS
Captured Signals | Microphone High sampling rate High speech quality | Motion Sensor Low sampling rate Low speech quality
Type of Voices | Human subjects: Arbitrary # of voices profiles | Machine-rendered: Limited # of voices profiles
Type of Speech | VUI requests: Arbitrary format | VUI responses: More deterministic format

## Slide 10: Attacking Requirements and Targets
Targeted permissions:
Read calendar
Read contacts, SMS
Read search history
Access coarse location
Access GPS trace
etc.
Affordable Attack
High attacking success rate
Explicit permission-protected private information extraction

## Slide 11: Challenge 1: how to achieve affordable attack?
Neither the smartphone OS nor the user can notice the attack.
Low on-device computational cost
  Real-time two-stage detection algorithm  < 5% Peak CPU Usage
  Lightweight voice identification DNN models.  79.6 KB model size
Low on-device storage cost
  Only save the potential MSS  16 kB/ response
Low communication requirement
  Only upload the private information  less than 50 bytes/ response
MSS Streaming
Real-time Detect, Segment, Identify the VUI responses
Process the MSS and extract the
on the cloud

## Slide 12: Challenge 2: Inferring Privacy from a Single VUI response  SLU model design
MSS Streaming
ASR
Got it, check
bank account 1234.
NLU
Type: Reminder
Intents:
Check bank account
1234
However, due to the low sampling rate and low speech quality, the first stage, i.e., ASR, can only achieve low accuracy.

## Slide 13: End-to-end SLU Model
MSS Streaming
End-to-end
SLU
Type: Reminder
Intents:
Check bank account
1234
The format of VUI response is deterministic.
Only need to extract the private information while ignoring other information.

## Slide 14: VUI Commands Generation
44,691 different VUI commands
23 types of VUI commands
Analysis the format and structures of VUI response, and then manually label them (1,000 hours to label 100 hours data).
Open-sourced dataset and code: https://github.com/Samsonsjarkal/StealthyIMU

## Slide 15: SLU Model Design
End-to-end SLU model
Seq-to-seq model
Encoder + Decoder design
Sub-word level Tokenizer
Teacher-forcing
How to improve the performance through crossmodal data?

## Slide 16: Knowledge Distillation from Speech-based SLU
Speech-based SLU achieves significantly better performance than the MSS-based.
Use the knowledge from the Speech-based SLU to help the training of the MSS-based SLU.

## Slide 17: Evaluation: VUI Response Private Entity Recognition
Lower TER, SEER, SER means better performance.
SLU model significantly outperforms the traditional ASR + NLU solution.
Knowledge distillation from speech signals can help
Evaluation metrics:
TER: Type Error Rate
SEER: Single Entity Error Rate
SER: Sentence Error Rate  only if all the entities in a single VUI response are recognized correctly

## Slide 18: Challenge 3: Extract the Explicit Permission-protected Privacy
Combining the private intents from single or multiple VUI responses.
One-time Stealing
Short-term Contextual Inference
Long-term Monitoring

## Slide 19: One-time Stealing
Take a single VUI response as the input to extract privacy information.
An average 85.28% success rate
Voice commands like
  Reminders
  Media Alarm
  Hands Free Calling
  Navigation App
  has complicated response formats resulting in relatively low success rate (> 70%).

## Slide 20: Short-term Contextual Inference
Infer private information using multiple consecutive VUI responses.
Example: Navigation app to recover GPS trace

## Slide 21: Short-term Contextual Inference
GPS trace recovery algorithm:
average/max deviation is 133 m/420 m

## Slide 22: Long-Term Monitoring
Repeat the same type of voice commands in a few days, like check weather, air quality, reminder, and navigate home, etc.
Assumption: each VUI response is a single individual event.
Identify the city name increases from 70% (1 inquiry) to above 98% (3+ inquiries).
Extract the city name from daily weather VUI response.

## Slide 23: Long-term Monitoring
Achieves 11 meters home address estimation error by combining 10 attempts.
Extract the home address from daily navigation back to home.

## Slide 24: Conclusion
Uses zero-permission motion sensors to extract permission-protected private information from VUI responses.
Affordable attack vector.
Formulate it to SLU problem, use cross-modal knowledge distillation strategy to extract the private entities.
Short-term and long-term attack to steal user calendar, search history, GPS trace, home address, etc.
Speech pre-distortion defense mechanism.
StealthyIMU will be general to use other side channels, like RF, light, etc, to steal the private information from other VUI devices.

## Slide 25
Thank you
Q&A
https://github.com/Samsonsjarkal/StealthyIMU

## Slide 26: StealthyIMU Attacking Pipeline
MSS Streaming
Process the MSS, extract the privacy
on the cloud
Real-time Detect, Segment, Identify the VUI responses
Process the MSS
on device
Process the MSS
on device
“Network in the background” permission, 100 KB/min
“Storage in the memory” permission, 100 KB/min
“Storage in the app” permission, 16 kB/ response
“Network” permission
“Network” permission
Attacker
Attacker
Attacker

## Slide 27: Real-time Detect, Segment VUI Responses
Two-stage detection
  Stage 1: Lightweight detection
    15 mW, 2% CPU
  Stage 2: Resample + FFT + detection
    35 mW, 5% CPU
Segmentation
  2~8 s duration for each VUI response
  16 KB per VUI response

## Slide 28: Offline Identify VUI Responses
Motivation: Identify the VUI response-induced MSS.
Assumption: VUIs only has a limited set of voice profiles.
Solution: Lightweight voice identification DNN models.

## Slide 29: Evaluation: Detect, Segment, and Identify VUI Responses
An average 3.5% EER for different voices
Equal Error Rate (EER)  both acceptance and rejection errors are equal.
 | Mobile Data | Segment Memory | Peak CPU | Power
Cloud-based attack | 100 KB/min | / | / | /
StealthyIMU | / | 16 KB/Seg | 5% | 35mW

## Slide 30: MSS and Corresponding Speech Collection
Set a reminder to check my bank account XXXX.
Text-to-speech
Motion Sensor
Microphone
ASR
Label
Bank account: XXXX

## Slide 31: Extract the Ground Truth Private Entities
Intents:
Turn left/ right
Take the next left/ right
Slight left/ right
Keep left/ right
Continue
Stay
Name:
Road
Highway
Exit name
Use the right lane to take exit 1b toward B drive then turn left onto C street Type: navigation Entities: type: intent | filler: take, type: name | filler: exit 1b;
type: intent | filler: towards, type: road | filler: B drive;
type: intent | filler: turn left, type: name | filler: C street;
Take (highway and exit)
Towards
Make a U-turn
Merge
Follow sign
Arrive at destination

## Slide 32: Evaluation: VUI Response Private Entity Recognition
Our SLU model can recognize 176 voice-associated segments with less than 1% battery consumption.

## Slide 33: Defense
Predistortion of Speech Signals
  Assumption: the highest MSS sampling rate < 500 Hz
  Insight: modifying the low modifying the low-frequency components of speech signals
    Will significantly impact the MSS.
    Will not affect the human perceivable speech quality.

## Slide 34: Defense
Redesigning the Permissions
  If vendors unleash the sampling rate limitation to 4000 Hz
Even if future smartphone OS restricts the motion sensor permission, the StealthyIMU attack can still work—it can pretend to be an innocuous app that needs the motion sensor permission alone.

## Slide 35: Evaluation: Generalization
Different Sampling Rate, Smartphone models
Different Motion Artifacts Interference

## Slide 36: Evaluation: Implementation & Overhead
Attack Implementation:
36
MSS Streaming
Real-time Detect, Segment, Identify the VUI responses
Process the MSS and extract the
on the cloud
Process the MSS, extract the privacy
on the cloud
 | Mobile Data | Segment Memory | Peak CPU | Power
1 | 100 KB/min | / | / | /
2 | / | 16 KB/Seg | 5% | 35mW
Voice detection and segmentation overhead (running in the background)

## Slide 37: Evaluation: System Overhead
On-device DNN overhead (running when the app is active)
Overall, the on-device implementation of StealthyIMU is unlikely to be distinguishable from an innocuous app.